## Slide 1: Using Amateur Radio Digital Modes
Joe Cupano, NE2Z
HOPE XV
Notes: 1

## Slide 2: Disclaimer
To perform any of the exercises within this workshop you either MUST have an FCC Technician Class license or greater
OR
perform the exercises under the supervision of someone holding an FCC Technician Class license or greater agreeing to act as control operator.

## Slide 3: Disclaimer (2)
Workshop attendees are required to have the pre-requisite hardware listed in the workshop. Please pair up with thos who may not have kit.

## Slide 4: Disclaimer (3)
Material provided does not present itself as an authoritative guide on the topic of Digital Modes and is an introductory only
In some cases, we take the most expedient route in conveying an idea at the sacrifice of some technical detail to avoid confusion.
The workshop is structured to provide a path of least resistance to quickly experience Digital Modes and inspire your interest in Amateur Radio.

## Slide 5: Onward . . .

## Slide 6: Overview of Amateur Radio
• Popular hobby and service that brings people, electronics and communication together
• Uses radio frequencies designated for licensed amateur radio operators for non-commercial exchange of messages, wireless experimentation, self-training, private recreation, contesting, and emergency communications
• Encryption is not generally permitted
• Is the only hobby governed by international treaty

## Slide 7: US Technician Class VHF/UHF Privileges

## Slide 8: 2 Meter Band Plan
Notes: While the FCC regulates what frequencies and where modes
are used by Amateur Radio operators, this gets broken down
further as informal agreements among Amateur Radio
operators as to where specific modes are used. These
informal agreements are referred to as Band plan or
Considerate Operators Guide.

## Slide 9: Modulation
Notes: Continuous Wave (CW)
Communication starts off with a radio wave carrier signal (aka carrier signal) that we impart an
intelligence onto. The simplest form of intelligence we can impart is simply turning the carrier on and
off in some rhythmic fashion. CW is the simplest form of communication with the on-off rhythm being
Morse Code. CW is arguably the original digital mode.
Amplitude Modulation (AM)
While turning a carrier on and off rhythmically gets the job done
albeit slowly, we could instead impart an audio signal on top of
the signal. Varying the amplitude of the carrier signal with audio
is AM. A refinement of AM that makes efficient use of power
and bandwidth is Single-Sideband (SSB.) More about this mode
will be discussed in the next section
Frequency Modulation (FM)
Varying the frequency of the carrier signal with audio is FM.
Each has advantages/disadvantages according to the radio
spectrum they are used on.

## Slide 10: Bandwidth
• AM modulation produces upper and lower sidebands on either side of the carrier signal which can lead to a total bandwidth twice the highest audio signal, around 6 Khz.
SSB is a refinement of AM that makes efficient use of power and bandwidth by suppressing the carrier signal and one of the sidebands
  either Lower Sideband (LSB) or Upper Sideband (USB.)
With radio spectrum a precious limited resource, the bandwidth of a signal limits how many simultaneous communications can occur within a given piece of spectrum.
Notes: Another dimension to our communication is how wide our resulting signal is measured as bandwidth.
AM modulation produces upper and lower sidebands on either side of the carrier signal which can lead
to a total bandwidth twice the highest audio signal, around 6 Khz.
SSB is a refinement of AM that makes efficient use of power and
bandwidth by suppressing the carrier signal and one of the sidebands
sending either Lower Sideband (LSB) or Upper Sideband
(USB.)

## Slide 11: Bandwidth (2)
• FM 15 Khz
• AM 6 Khz
• SSB 3 Khz
• CW 100 Hz
Notes: To give you context on bandwidth sizes, here is a list of modes
and their average bandwidth.
• FM 15 Khz
• AM 6 Khz
• SSB 3 Khz
• CW 100 Hz
With radio spectrum a precious limited resource, the bandwidth of a signal limits how many
simultaneous communications can occur within a given piece of spectrum.

## Slide 12: Modulation & Bandwidth Visual
FM
AM
LSB
USB

## Slide 13: Performance
• Signals travel across an atmosphere fraught with natural and man-made phenomenon that can impact the integrity of a signal
When we talk about performance in Amateur Radio communications, we are looking at the best way to communicate intelligence expediently and reliably without loss of integrity across varying atmospheric conditions using minimal power and making efficient use of radio spectrum.
Performance is where digital modes excel.
Notes: Radio waves travel across an atmosphere fraught with natural and man-made phenomenon that can impact the integrity of that signal. If you’ve listened to AM radio before/during/after a thunderstorm you hear various noises interfering with your ability to hear a song or what is being said. Listen in the evening anf you may hear signals fade in and out according to upper atmospheric conditions. Mind you, these radio stations are using kilowatts of power using Amplitude Modulation consuming significant bandwidth.
When we talk about performance in Amateur Radio communications, we are looking at the best way to communicate intelligence expediently and reliably without loss of integrity across varying atmospheric conditions using minimal power and making efficient use of radio spectrum. Performance is where digital modes excel.

## Slide 14: Digital Modes
Rooted in 1’s and 0’s in some fashion.
Frequency Shift Keying (FSK)
  Shifting the frequency of a signal with one frequency represent 0’s and another representing 1’s
Audio Frequency Shift Keying (AFSK)
  Differing audio tones upon a signal with one tone representing 0’s and another representing 1’s
  Audio levels are critical to success
  When audio levels set correctly AFSK presents the same signal as FSK
Notes: Digital communications is rooted in our ability to communicate 1’s and 0’s in some fashion. Methods include:
Keying a signal on and off as with CW
Shifting the frequency of a signal with one frequency represent 0’s and another representing 1’s
Differing audio tones upon a signal with one tone representing 0’s and another representing 1’s
Let’s dig into this further.
Frequency Shift Keying (FSK)
FSK is a frequency modulation scheme in which intelligence is transmitted digitally as frequency changes in a carrier signal. One frequency may represent 1’s (referred to as the MARK frequency) and the other frequency as 0’s (referred to as the SPACE frequency.)
The first digital mode to employ this method was Radio Teletype (RTTY.) RTTY was an evolution in the 1920’s of early landline teleprinter communications that began in the mid-1800’s. For RTTY the signal is shifted 170 Hz. More about RTTY later.
Audio Frequency Shift Keying (AFSK)
AFSK is a modulation scheme in which intelligence is transmitted digitally as audio pitch changes on a carrier signal whether it be AM or FM. Audio often transitions between two tones representing 1’s and 0’s respectively.
AFSK vs FSK
While AFSK allows you the flexibility to use sound cards on computers to generate tones as used by various digital modes, you need to insure your audio levels (sending and listening) are set correctly to insure you do not overdrive audio and generate distorted signals. When levels are set correctly, AFSK gives you the same signal as FSK.
All of the digital mode usage in this workshop will use AFSK.

## Slide 15: CW and Modulated CW (MCW)
Modulated continuous wave (MCW) is Morse code telegraphy transmitted using an audio tone to modulate a carrier wave.
Continuous wave (CW), by contrast, does not use a subcarrier, so there is no emission at all between Morse code symbols
Notes: MCW
We mentioned CW as the first digital mode whose method of communicating intelligence is simply turning the carrier on and off in the motion of Morse Code. Another method of sending Morse Code is using Modulated Continuous Wave. With MCW we send an on/off audio tone in the rhythm of Morse Code. An example of MCW on FM is hearing a VHF/UHF repeater ID in Morse Code.
Though MCW is switching between audio tone and off as compared to two different tones, you could consider MCW a form of AFSK. Important to note that within the US, MCW cannot legally be used on HF bands but can be used on VHF and higher frequencies

## Slide 16: Radioteletype (RTTY)
FSK signal that shifts 170 Hz.
1 is MARK frequency, 0 SPACE frequency.
Baudot Character set
Paper Rolls, Punch Tape, and a Bell.
Notes: RTTY
Evolution of early landline teleprinter communications that began in the mid-1800’s. RTTY began around the 1920’s using FSK with a signal that shifted 170 Hz. One frequency represents a 1 (referred to as the MARK frequency) and another frequency as 0 (referred to as the SPACE frequency.)
As a method of keyboard-to-keyboard communication, RTTY used a five-bit code called Baudot to represent letters, numbers, punctuation, and some control characters. Since the output was printed on rolls of teletype paper, some of the control characters were necessary to signify carriage return and linefeed of the paper. There was control character for ringing a bell on a teletype as well.
Over time teleprinters were replaced with terminals and then eventually with PCs the use of ASCII akll but replacing Baudot. Since AFSK gives you the same signal as FSK, dedicated RTTY modems of the past became replaced with sound cards on PC’s. As a reminder when using AFSK, audio levels are critical for proper reception and clean transmission of signals.

## Slide 17: PSK31
Uses binary phase shift keying (BPSK)and a special code (Varicode) to achieve character rates similar to RTTY (50 wpm) in a much narrower bandwidth
Better error rate than RTTY on noisy channels
Lower RF power requirement
0 0 1 0 0
phase phase no phase
shift shift shift shift
Notes: Many of the digital modes that are popular today are born as PC implementations using sound card and radio interfaces rather than implements as dedicated hardware devices like CW and RTTY. PSK31 uses amplitude and phase modulation converted to audio. We say phase modulation because the phase shift of the signal determines whether you are sending a 0 or a 1 (180-degree phase shift and no phase shift respectively.)
PSK31 is designed as a keyboard-to-keyboard communication protocol so its data rate of 31 baud is designed to be close to typing speed. The mode is very efficient as we will learn during our lab exercises.

## Slide 18: MT63
Used on VHF/UHF by Amateur Radio Emergency Services organizations for message handling.
The mode provides Forward Error Correction (FEC) and 2 Khz of bandwidth providing transfer rates of 1 KB/minute.
I know the transfer rate does not sound like much compared to a WiFi connection but at this rate on VHF/UHF frequencies using an omni-directional antenna depending on terrain, range goes from tens of miles to a hundred miles.
Notes: MT63-2000L
Up till now we’ve been covering modes used mostly on HF that are slow and have no error correction. MT63 is a digital mode used on VHF/UHF by Amateur Radio Emergency Services organizations for message handling. The mode provides Forward Error Correction (FEC) and 2 Khz of bandwidth providing transfer rates of 1 KB/minute. I know the transfer rate does not sound like much compared to a WiFi connection but the range at this rate with an omni-directional antenna depending on terrain, go from of tens of miles to almost one hundred.

## Slide 19: FT8
Popular for its ability to send signals despite challenging propagation conditions, high noise environments, low power operations (QRP), or even compromised antennas.
Transmits and receives only the bare essentials needed to make a contact in a semi-automated timed fashion.
Not a "keyboard-to-keyboard" (real-time chat) mode.
Notes: MT63-2000L
Up till now we’ve been covering modes used mostly on HF that are slow and have no error correction. MT63 is a digital mode used on VHF/UHF by Amateur Radio Emergency Services organizations for message handling. The mode provides Forward Error Correction (FEC) and 2 Khz of bandwidth providing transfer rates of 1 KB/minute. I know the transfer rate does not sound like much compared to a WiFi connection but the range at this rate with an omni-directional antenna depending on terrain, go from of tens of miles to almost one hundred.

## Slide 20: FT8
80M on 3.573 MHz
40M on 7.071 MHz and 7.074 MHz
30M on 10.136 MHz
20M on 14.074 MHz
17M on 18.1 MHz
6M on 50.313 MHz and 50.323 MHz
2M on144.174 MHz,
70cm on 432.061 MHz and 432.174 MHz
Notes: MT63-2000L
Up till now we’ve been covering modes used mostly on HF that are slow and have no error correction. MT63 is a digital mode used on VHF/UHF by Amateur Radio Emergency Services organizations for message handling. The mode provides Forward Error Correction (FEC) and 2 Khz of bandwidth providing transfer rates of 1 KB/minute. I know the transfer rate does not sound like much compared to a WiFi connection but the range at this rate with an omni-directional antenna depending on terrain, go from of tens of miles to almost one hundred.

## Slide 21: What about <INSERT MODE HERE>
Did I say this was an introductory workshop
Learning digital mode fundamentals is best when referencing established modes and understand the attributes that contribute to their longevity.
No matter what protocol comes along, you have an understanding of its fundamentals.

## Slide 22: Caveats
When using AFSK for digital modes so sound levels will be CRITICAL
Using the VHF/UHF spectrum and low power eliminates band conditions as a variable to be considered in lab exercises.
When using FM, we will be subject to a phenomenon known as the capture effect ,which will interfere with our ability to show how multiple signals simultaneously share a frequency as done on HF with SSB.

## Slide 23: Labs
Setup and functional test of the Baofeng UV-5R radio
Setting up the USB Audio
Setup Digital modes software
Making your First Contact
Experimentation

## Slide 24: Lab 1: Setting up the Radio
Setup and functional test of the Baofeng UV-5R radio.

## Slide 25: Lab 2: Setting up the USB Audio
Setup and functional test of external USB sound device.
Remember for many OS the MASTER level needs to be set as well.

## Slide 26: Lab 3: Set up Digital Mode Software
Installation and setup of the digital mode software.

## Slide 27: Lab 4: First Contact
Keep checking Audio Levels.
Frequencies we use in class
  CHAN1
  CHAN2
  CHAN3
  CHAN4

## Slide 28: Lab 5: Experimentation
Get familiar with various digital modes understanding their strengths and weaknesses.

## Slide 29: Thank you !